## Slide 1
C Pointers
COMPENG 2SH4 Topic 7
Dr. Shahrukh Athar
Credit: The current version of these slides has been developed by Dr. Scott Chen (2SH4 F23 C02). I am using these slides with his permission and have made only slight modifications.

## Slide 2
Agenda
Address-Data Duality
  Reference (Address) Operator &
  Dereference (Indirection) Operator *
Pointers
  Working with Pointers
  Pass-by-Reference vs. Pass-by-Value
  Simulating Multiple Return Values

## Slide 3: Address-Data Duality
Reference and Dereference Operators
Watch Before Lecture:
[PLV 7-1] Computer Memory Structure
[PLV 7-2] Address-Data Duality

## Slide 4
C allows us to refer to the address of a memory location of a variable
  Address Operator (aka. Referencing Operator):
  Conversion Specifier for Hexadecimal-Formatted Memory Address - %p
    Can also use %x (Hex-Formatted Integer), but most compilers will complain with warning
Address (Referencing) Operator &
#include <stdio.h>
int main(void)
{
int n = 6;
printf(“Variable n is located at address: %p\n”, &n);
printf(“Variable n holds a value of: %d\n”, n);
return 0;
} // end of main()
Referencing Operator &
Request for memory address of a variable
L7Ex1-RefOp.c
Assuming
&n = 0x 0061FF1C
n = 6 (0x 00000006)
00 (0b 00000000)
00 (0b 00000000)
06 (0b 00000110)
0x 0061FF1C
0x 0061FF1D
0x 0061FF1E
00 (0b 00000000)
0x 0061FF1F
0b (0%) prefix indicates
Binary Number

## Slide 5
C allows us to refer to the address of a memory location of a variable
  GOTCHA!
    Referencing Operator cannot be applied to rvalues (i.e. constants, constant expressions)
      &1934 // Syntax Error
      &(y + 5) // Syntax Error
    Answer:
      rvalues are temporarily stored on Stack
        Address available, but access not permitted by C
      Some rvalues are stored inside the CPU registers
        No address available whatsoever
      Therefore, & can only be applied to an lvalue (value-holding variables)
Address (Referencing) Operator &
Think about why

## Slide 6
Address-Data Duality Diagram (Part I)
  More to come…
Address (Referencing) Operator &
int var = 3;
“var” 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
Data
printf(“%d”, var);
// prints “3” (value)
Address
Referencing Operator
&
printf(“%p”, &var);
// prints “0061FF20” (address)

## Slide 7
Arrays in Memory
Recall! – Array Name is the Address of the First Element of the Array
  Let’s now validate this claim with the Reference Operator
Recall! – Array subscript is the offset index from the first element
Recall! – C does not stop you from accessing array out of bounds
  b[3] Accessing 3 locations positively offset from the first element (will compile)
  b[-2] Accessing 2 locations negatively offset from the first element (will compile)
#include <stdio.h>
int main(void)
{
int b[3] = {1, 2, 3};
printf(“b[0] has a value of %d at Address 0x%p\n”, b[0], &b[0]);
printf(“b[1] has a value of %d at Address 0x%p\n”, b[1], &b[1]);
printf(“b[2] has a value of %d at Address 0x%p\n”, b[2], &b[2]);
printf(“Array Name points to Address 0x%p\n”, b);
return 0;
} // end of main()
L7Ex2-ArrayName.c
If lucky, it works
Typically, garbage result
If unlucky, seg fault

## Slide 8
Pointer – Address-Holding Variable
Address-Holding Variable “Pointer” – holding addresses
  A new data type - with different variations
  Integer Pointer Holds address of an integer variable
  Float Pointer Holds address of a float variable
  Character Pointer Holds address of a character variable
  Double Pointer Holds address of a double variable
  A more precise definition of Pointer variable type
    Its allowed value is the memory address of a memory slot
    This memory slot may or may not be used by a variable
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
var is an Integer Variable
ptr is an Integer Pointer
This name is tricky… Double Precision Float Pointer to be clear

## Slide 9
Pointer – Address-Holding Variable
Address-Holding Variable “Pointer” – holding addresses
    Its allowed value is the memory address of a memory slot
  How to define and assign value to ptr from var?
    Declare the integer pointer variable ptr
    Assign address of var as the value to ptr
    Verify
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
var is an Integer Variable
ptr is an Integer Pointer
int* ptr; // can also be int *ptr;
ptr = &var; // & gives address!
int var = 3;
int* ptr = &var;
printf(“var = %d at 0x%p\n”, var, &var);
printf(“ptr points to Address 0x%p\n”, ptr);
L7Ex3-PtrBasic.c

## Slide 10
Pointer – Address-Holding Variable
Address-Holding Variable “Pointer” – holding addresses
    Its allowed value is the memory address of a memory slot
    A new data type - with different variations
  How to declare different pointer variables?
    data type keyword + * (Dereferencing Operator)
    int *nPtr; Declare an integer pointer
    int* nPtr; Same as above
    char* chPtr; Declare a character pointer
    float *fPtr; Declare a float pointer
    double *dPtr; Declare a double (precision) pointer
  When assigning address to a variable…
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
var is an Integer Variable
ptr is an Integer Pointer
ptr = &var; // “ptr points to variable var”

## Slide 11
Indirection (Dereferencing) Operator *
Unary Operator – NOT multiplication
Two Purposes
  Declaring Pointers – Applies to the end of a Data Type
    Effect: Instruct the computer to treat the value as address
  Applies to the head of a Pointer or Expression of Pointer Type
    Effect: Returns value of the variable the pointer points to
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
var is an Integer Variable
ptr is an Integer Pointer
int var = 3;
int* ptr = &var;
printf(“var = %d at 0x%p\n”, var, &var);
printf(“ptr points to Address 0x%p\n”, ptr);
printf(“ptr points to a Value of %d\n”, *ptr);
L7Ex3-1-Deref.c

## Slide 12
Indirection (Dereferencing) Operator *
Unary Operator – NOT multiplication
Two Purposes
  Applies to a Pointer or Expression of Pointer Type
    Effect: Returns the variable the pointer points to
    Implication:
      If ptr points to var, *ptr is another name for var
      *ptr can be used in place of var anywhere, anytime
      *ptr can be used on the left of an assignment
      Modifying the value through *ptr will…
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
var is an Integer Variable
ptr is an Integer Pointer
Directly modify the value in var!!

## Slide 13
Indirection (Dereferencing) Operator *
Unary Operator – NOT multiplication
Two Purposes
  Applies to a Pointer or Expression of Pointer Type
    Returns the variable the pointer points to
    Modifying the value of a dereferenced pointer will modify the genuine value of the pointed variable
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
var is an Integer Variable
ptr is an Integer Pointer
int var = 3;
int* ptr = &var;
printf(“var = %d at 0x%p\n”, var, &var);
printf(“ptr points to Address 0x%p with Value %d\n”, ptr, *ptr);
*ptr *= 10; // same as var *= 10, i.e., var = var * 10
printf(“var = %d at 0x%p\n”, var, &var);
printf(“ptr points to Address 0x%p with Value %d\n”, ptr, *ptr);
L7Ex3-2-DerefMod.c

## Slide 14
Address-Data Duality Diagram
int var = 3;
Data
printf(“%d”, var);
// prints “3” (value)
Address
Referencing Operator
&
printf(“%p”, &var);
// prints “0061FF20” (address)
0x0061FF20
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“ptr”
(int) 3
??
??
0x 0061FF1C
0x 0061FF20
0x 0061FF24
“var”
int* ptr = &var;
printf(“%p”, ptr);
// prints “0061FF20” (address)
*
Dereferencing Operator
printf(“%d”, *ptr);
// prints “3” (value)
*ptr behaves as an alias of var

## Slide 15: Operations on Pointers
Watch Before Lecture:
[PLV 7-3] Passing Data by Pointer or Reference

## Slide 16
Assigning Values to Pointers
Declared pointer can accept the following values
  The address of a matching-type variable through referencing operator
  NULL pointer (integer value 0x0, points to “nothingness”)
    Use it to initialize pointer variables
    Cannot be dereferenced per runtime restriction
  A pointer of the same type
int var = 3;
int* ptr = &var;
double dVar = 2.6631;
double* dPtr = &dVar;
char* cPtr = NULL;
unsigned long* ulPtr = 0; // same as NULL (0x0)
double* dPtr2 = dPtr;
unsigned long* ulPtr2 = ulPtr;
If allowed, will Seg Fault
A lot more to it... But out of scope

## Slide 17
Assigning Values to Pointers
Declared pointer can accept the following values
  A pointer of the same type – Example
#include <stdio.h>
int main(void)
{
int *nPtr1 = NULL, *nPtr2 = NULL; // both int pointer
int n = 0; // int type
// can also do int *nPtr1 = NULL, *nPtr2 = NULL, n;
return 0;
} // end of main()
(int) 0
??
??
0x 0053A0DC
0x 0053A0E0
0x 0053A0E4
“n”
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“nPtr1”
??
??
0x 003D00F9
0x 003D00FD
0x 003D0101
“nPtr2”
NULL (0)
NULL (0)

## Slide 18
Assigning Values to Pointers
Declared pointer can accept the following values
  A pointer of the same type – Example
#include <stdio.h>
int main(void)
{
int *nPtr1 = NULL, *nPtr2 = NULL; // both int pointer
int n = 0; // int type
// can also do int *nPtr1 = NULL, *nPtr2 = NULL, n;
nPtr1 = &n;
nPtr2 = nPtr1;
// both *nPtr1 and *nPtr2 are now aliases of n
// all three can now be interchangeably used
return 0;
} // end of main()
(int) 0
??
??
0x 0053A0DC
0x 0053A0E0
0x 0053A0E4
“n”
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“nPtr1”
??
??
0x 003D00F9
0x 003D00FD
0x 003D0101
“nPtr2”
NULL (0)
NULL (0)
0x0053A0E0
0x0053A0E0

## Slide 19
Assigning Values to Pointers
Declared pointer can accept the following values
  A pointer of the same type – Example
#include <stdio.h>
int main(void)
{
int *nPtr1 = NULL, *nPtr2 = NULL; // both int pointer
int n = 0; // int type
// can also do int *nPtr1 = NULL, *nPtr2 = NULL, n;
nPtr1 = &n;
nPtr2 = nPtr1;
// both *nPtr1 and *nPtr2 are now aliases of n
// all three can now be interchangeably used
*nPtr2 = 76;
return 0;
} // end of main()
??
??
0x 0053A0DC
0x 0053A0E0
0x 0053A0E4
“n”
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“nPtr1”
??
??
0x 003D00F9
0x 003D00FD
0x 003D0101
“nPtr2”
0x0053A0E0
0x0053A0E0
(int) 0
(int) 76

## Slide 20
Assigning Values to Pointers
Declared pointer can accept the following values
  A pointer of the same type – Example
#include <stdio.h>
int main(void)
{
int *nPtr1 = NULL, *nPtr2 = NULL; // both int pointer
int n = 0; // int type
// can also do int *nPtr1 = NULL, *nPtr2 = NULL, n;
nPtr1 = &n;
nPtr2 = nPtr1;
// both *nPtr1 and *nPtr2 are now aliases of n
// all three can now be interchangeably used
*nPtr2 = 76;
++*nPtr1; // Will be interpreted as ++(*nPtr1);
return 0;
} // end of main()
??
??
0x 0053A0DC
0x 0053A0E0
0x 0053A0E4
“n”
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“nPtr1”
??
??
0x 003D00F9
0x 003D00FD
0x 003D0101
“nPtr2”
0x0053A0E0
0x0053A0E0
(int) 76
(int) 77
Unary operators have the same precedence level and associated Right-to-Left

## Slide 21
Assigning Values to Pointers
Declared pointer can accept the following values
  A pointer of the same type – Example
#include <stdio.h>
int main(void)
{
int *nPtr1 = NULL, *nPtr2 = NULL; // both int pointer
int n = 0; // int type
// can also do int *nPtr1 = NULL, *nPtr2 = NULL, n;
nPtr1 = &n;
nPtr2 = nPtr1;
// both *nPtr1 and *nPtr2 are now aliases of n
// all three can now be interchangeably used
*nPtr2 = 76;
++*nPtr1; // Will be interpreted as ++(*nPtr1);
return 0;
} // end of main()
??
??
0x 0053A0DC
0x 0053A0E0
0x 0053A0E4
“n”
??
??
0x 0061F002
0x 0061F006
0x 0061F00A
“nPtr1”
??
??
0x 003D00F9
0x 003D00FD
0x 003D0101
“nPtr2”
0x0053A0E0
0x0053A0E0
(int) 77
L7Ex4-PtrAssign.c

## Slide 22
Passing Pointers into a Function
Pass-by-Value Mode
  All parameters are passed into function by value (copied)
  Modifications on the values only reflect on the copied values
Passing Pointers into a Function is – by value too!
  Nevertheless, the value of a pointer is the address of a variable
  Thus, by applying the dereferencing operator on this address within the function…
    We can modify the Genuine Value of the pointed variable
  This is known as Pass-by-Reference Mode
    The address of the variable is copied into the function instead of its value
    With the address, the function can directly access the memory location of a variable (by *)
      All modifications on the value will then be applied onto the original variable
C’s way to “simulate“ Pass-by-Reference
(This is actually Pass-by-Pointer)
C++ has a more intuitive Pass-by-Reference setup

## Slide 23
Pass by Reference – Using Pointer
Example – Swapping 2 Variables
  Setup – Two variables in main() and a swap() function
  End Result – Pass two variables into swap() using pass-by-reference, Two values swapped in main() after swap() completed
int main(void)
{
int a = 100;
int b = 200;
// swap two vars
swap( &a, &b );
return 0;
}
200
100
Memory
a
b
0x 5AE4
0x 5AE8
Pass the addresses
void swap( int *xPtr, int *yPtr )
{
int temp;
}
Temp Mem
xPtr
yPtr
0x 83B1
0x 83B5
Catch addresses with Pointers
0x 5AE4
0x 5AE8
Equivalence
xPtr = &a; yPtr = &b;
0x 83B9
temp
xPtr points to a (*xPtr is another name of a) yPtr points to b (*yPtr is another name of b)

## Slide 24
Pass by Reference – Using Pointer
Example – Swapping 2 Variables
  Setup – Two variables in main() and a swap() function
  End Result – Pass two variables into swap() using pass-by-reference, Two values swapped in main() after swap() completed
int main(void)
{
int a = 100;
int b = 200;
// swap two vars
swap( &a, &b );
return 0;
}
200
100
Memory
a
b
0x 5AE4
0x 5AE8
Pass the addresses
void swap( int *xPtr, int *yPtr )
{
int temp;
temp = *yPtr; // temp = b
}
Temp Mem
xPtr
yPtr
0x 83B1
0x 83B5
Catch addresses with Pointers
0x 5AE4
0x 5AE8
Equivalence
xPtr = &a; yPtr = &b;
0x 83B9
temp
xPtr points to a (*xPtr is another name of a) yPtr points to b (*yPtr is another name of b)
200

## Slide 25
Pass by Reference – Using Pointer
Example – Swapping 2 Variables
  Setup – Two variables in main() and a swap() function
  End Result – Pass two variables into swap() using pass-by-reference, Two values swapped in main() after swap() completed
int main(void)
{
int a = 100;
int b = 200;
// swap two vars
swap( &a, &b );
return 0;
}
100
Memory
a
b
0x 5AE4
0x 5AE8
Pass the addresses
void swap( int *xPtr, int *yPtr )
{
int temp;
temp = *yPtr; // temp = b
*yPtr = *xPtr; // b = a
}
Temp Mem
xPtr
yPtr
0x 83B1
0x 83B5
Catch addresses with Pointers
0x 5AE4
0x 5AE8
Equivalence
xPtr = &a; yPtr = &b;
0x 83B9
temp
xPtr points to a (*xPtr is another name of a) yPtr points to b (*yPtr is another name of b)
200
100
200

## Slide 26
Pass by Reference – Using Pointer
Example – Swapping 2 Variables
  Setup – Two variables in main() and a swap() function
  End Result – Pass two variables into swap() using pass-by-reference, Two values swapped in main() after swap() completed
int main(void)
{
int a = 100;
int b = 200;
// swap two vars
swap( &a, &b );
return 0;
}
Memory
a
b
0x 5AE4
0x 5AE8
Pass the addresses
void swap( int *xPtr, int *yPtr )
{
int temp;
temp = *yPtr; // temp = b
*yPtr = *xPtr; // b = a
*xPtr = temp; // a = temp
}
Temp Mem
xPtr
yPtr
0x 83B1
0x 83B5
Catch addresses with Pointers
0x 5AE4
0x 5AE8
Equivalence
xPtr = &a; yPtr = &b;
0x 83B9
temp
xPtr points to a (*xPtr is another name of a) yPtr points to b (*yPtr is another name of b)
200
100
100
200

## Slide 27
Pass by Reference – Using Pointer
Example – Swapping 2 Variables
  Setup – Two variables in main() and a swap() function
  End Result – Pass two variables into swap() using pass-by-reference, Two values swapped in main() after swap() completed
int main(void)
{
int a = 100;
int b = 200;
// swap two vars
swap( &a, &b );
return 0;
}
Memory
a
b
0x 5AE4
0x 5AE8
Pass the addresses
void swap( int *xPtr, int *yPtr )
{
int temp;
temp = *yPtr; // temp = b
*yPtr = *xPtr; // b = a
*xPtr = temp; // a = temp
}
Temp Mem
xPtr
yPtr
0x 83B1
0x 83B5
Catch addresses with Pointers
0x 5AE4
0x 5AE8
Equivalence
xPtr = &a; yPtr = &b;
0x 83B9
temp
xPtr points to a (*xPtr is another name of a) yPtr points to b (*yPtr is another name of b)
200
100
200
When swap() is done, all local variables (xPtr, yPtr, temp) are destroyed
L7Ex5-PassByRef.c

## Slide 28
Multiple Return Values – Using Pointer
One of the ways to simulate multiple return values
  Pass the input variables by value
    Such that the function will not accidentally modify the genuine input values
  Pass the desired variables to capture the output values by reference
    Such that the function can directly write the output values to the genuine variables
Example – A function calculating both the sum and difference of two integers
  Two operands as input variables
  Two results to return
  We will achieve the multiple return values using Pointers!

## Slide 29
Multiple Return Values – Using Pointer
Example – A function calculating both the sum and difference of two integers
  Setup – Two int operands and two int results in main()
  End Result – Pass two operands into sum_diff() by value, two results by reference Two results available in main() after sum_diff() completed
int main(void)
{
// Two Int Operands
int x = 10, y = 20;
// Two Int Results
int sum, diff;
// Calculate!
sum_diff( x, y, &sum, &diff );
return 0;
}
20
10
Memory
x
y
0x 5AE4
0x 5AE8
??
??
sum
diff
0x 5AEC
0x 5AF0
Pass the value
Pass the Address
void sum_diff(int a, int b, int* sumP, int* diffP)
{
}
Capture Value
Capture Address
Temp Mem
b
sumP
0x 83B0
0x 83B4
0x 83B8
diffP
a
0x 83AC
10
20
0x 5AEC
0x 5AF0

## Slide 30
Multiple Return Values – Using Pointer
Example – A function calculating both the sum and difference of two integers
  Setup – Two int operands and two int results in main()
  End Result – Pass two operands into sum_diff() by value, two results by reference Two results available in main() after sum_diff() completed
int main(void)
{
// Two Int Operands
int x = 10, y = 20;
// Two Int Results
int sum, diff;
// Calculate!
sum_diff( x, y, &sum, &diff );
return 0;
}
20
10
Memory
x
y
0x 5AE4
0x 5AE8
sum
diff
0x 5AEC
0x 5AF0
Pass the value
Pass the Address
void sum_diff(int a, int b, int* sumP, int* diffP)
{
*sumP = a + b; // same as sum = a + b;
}
Capture Value
Capture Address
Temp Mem
b
sumP
0x 83B0
0x 83B4
0x 83B8
diffP
a
0x 83AC
10
20
0x 5AEC
0x 5AF0
??
??
30

## Slide 31
Multiple Return Values – Using Pointer
Example – A function calculating both the sum and difference of two integers
  Setup – Two int operands and two int results in main()
  End Result – Pass two operands into sum_diff() by value, two results by reference Two results available in main() after sum_diff() completed
int main(void)
{
// Two Int Operands
int x = 10, y = 20;
// Two Int Results
int sum, diff;
// Calculate!
sum_diff( x, y, &sum, &diff );
return 0;
}
20
10
Memory
x
y
0x 5AE4
0x 5AE8
sum
diff
0x 5AEC
0x 5AF0
Pass the value
Pass the Address
void sum_diff(int a, int b, int* sumP, int* diffP)
{
*sumP = a + b; // same as sum = a + b;
*diffP = a – b; // same as diff = a – b;
}
Capture Value
Capture Address
Temp Mem
b
sumP
0x 83B0
0x 83B4
0x 83B8
diffP
a
0x 83AC
10
20
0x 5AEC
0x 5AF0
??
30
-10

## Slide 32
Multiple Return Values – Using Pointer
Example – A function calculating both the sum and difference of two integers
  Comprehension Tip - Do not think of sumP and diffP as pointers
  Instead – Think of *sumP as the original variable sum, intended for storing sum of a and b – Think of *diffP as the original variable diff, intended for storing difference of a and b
int main(void)
{
// Two Int Operands
int x = 10, y = 20;
// Two Int Results
int sum, diff;
// Calculate!
sum_diff( x, y, &sum, &diff );
return 0;
}
20
10
Memory
x
y
0x 5AE4
0x 5AE8
sum
diff
0x 5AEC
0x 5AF0
Pass the value
Pass the Address
void sum_diff(int a, int b, int* sumP, int* diffP)
{
*sumP = a + b; // same as sum = a + b;
*diffP = a – b; // same as diff = a – b;
}
Capture Value
Capture Address
Temp Mem
b
sumP
0x 83B0
0x 83B4
0x 83B8
diffP
a
0x 83AC
10
20
0x 5AEC
0x 5AF0
30
-10
L7Ex6-MultiReturn.c

## Slide 33
Takeaways
Memory Map
  C is designed to efficiently utilize memory
  To take advantage of the memory efficiency, pointers are needed
Address-Data Duality
  C allows free access of any lvalue data and its address interchangeably
  Address (Referencing) Operator &
  Indirection (Dereferencing) Operator *
Pointer
  A data type that accepts memory address of another variable
  (Simulated) Pass by Reference vs. Pass by Value
  Simulating multiple return values from functions

## Slide 34
Upcoming
Pointer Arithmetic
  Array Name Revisited
  Pointer-Offset Notation
  Pointer and String
  sizeof() Operator
Dynamic Memory Allocation